## Slide 1: Changes since Last Iteration
Bottom plate
Linear Seal

## Slide 2: Bottom Plate
The bottom plate was modified in two ways:
The holes for the BR penetrators were added
A raised structure was added to mimic the sealing done to the electronics enclosure

## Slide 3: Trelleborg Linear Shaft Seal
Seal used is a model available from the Trelleborg website and is used for 10mm shafts.
As far as I can tell they are designed to be press fit into the part

## Slide 4: Gripper with O-Ring
Max Diameter: 96mm (3.8 in)
Max Length: 172.75mm (6.8 in)
***Need to edit geometry to allow for pneumatic fittings to sit in first position***

## Slide 5
Gripper with Face Seal
Max Diameter: 96mm (3.8 in)
Max Length: 172.75mm (6.8 in)

## Slide 6: What’s next?
Which type of seal is best for NUGV?
  Face Seal vs O-ring seal vs something else(?)
Editing the finger geometry
  Remove planned bearing slot
Complete sourcing of parts if design chosen